## Slide 1
Marc Riedel
Associate Professor, Electrical and Computer Engineering University of Minnesota
ITA – Feb. 14, 2014 (“Singles’ Awareness Day”)
Probability as a State Variable for Nanoscale Computation
1,1,0,0,0,0,1,0
1,1,0,1,0,1,1,1
1,1,0,0,1,0,1,0
a = 6/8
c = 3/8
b = 4/8

## Slide 2: Positional Encodings
75710 = 7·102 + 5·101 + 7·100
A positional representation scheme is compact: 2n distinct numbers can be represented with n bits.
Operating on this representation is complex.
Human
Computer
10101112 = 26 + 24 + 22 + 21 + 20

## Slide 3: Multiplication
HA: Half adder, 2 basic gates (AND and XOR)
FA: Full adder, 5 basic gates (AND, OR, and XOR)
In total 30 gates!
a x b = c
Notes: Conventional multiplier works on binary radix encoded number. As any student in introductory course, it is complicated.

## Slide 4: Multiplication
1,1,0,0,0,0,1,0
1,1,0,1,0,1,1,1
1,1,0,0,1,0,1,0
a = 6/8
b = 4/8
c = 3/8
Assume two input bit streams are independent
6/8 · 4/8 = 3/8
a x b = c
Notes: Indeed, it is no a coincidence. Lower case letters represent probabilities…

## Slide 5: Representing a Value by a Sequence of Random Bits
A real value x in [0, 1] is represented by a sequence of random bits, each of which has probability x of being one and probability of 1 − x of being zero.
0,1,0,1,1,0,0
x = 3/7

## Slide 6: Serial versus Parallel
0,1,0,1,1,0, 0
Stochastic Bit Streams
x = 3/7
Probabilistic Bundles
x = 3/7
0
1
0
1
1
0
0
Notes: Probabilistic bundle is applicable to nanowire crossbar arrays.

## Slide 7: Physical Level
Nanowire Crossbar (Idealized)
A1
A2
A3
A4
A collection of inverters with shuffled outputs!
Notes: However, they are random.
In an ideal situation, each horizontal nanowire intersects with the doped region of exactly one of the vertical nanowires.

## Slide 8: Nanowire Crossbar Array
A1
A2
A3
A4
B1
B2
B3
B4
A4B3
A1B2
A2B4
A3B1
Shuffled AND
Notes: In my preliminary work, I have explored the ways in which the randomness due to self assembly can be used.

## Slide 9: Stochastic Logic
5/8
3/8
4/8
3/8
4/8
8/8
Probability values are the input and output signals.
combinational circuit

## Slide 10: Stochastic Logic
Probability values are the input and output signals.
1,1,0,1,0,1,1,0…
1,0,0,0,1,1,0,0,…
0,1,1,0,1,0,1,0,…
0,1,1,0,1,0,0,0,…
1,0,1,0,1,0,1,0,…
1,1,1,1,1,1,1,1,…
serial bit streams
combinational circuit

## Slide 11: Stochastic Logic
combinational circuit
Probability values are the input and output signals.
parallel bit streams
4/8
3/8
4/8
8/8
5/8
3/8

## Slide 12: Randomness
combinational circuit
Analog/digital interface with fractional weighting of 1’s.
parallel bit streams
A/D
A/D
A/D
D/A
D/A
A/D

## Slide 13: Arithmetic Operations
Multiplication
(Scaled) Addition
b
a
B
P
A
P
C
P
c
=
=
=
)
(
)
(
)
(
)
)
1
(
(
)]
(
1
[
)
(
)
(
)
(
b
s
a
s
B
P
S
P
A
P
S
P
C
P
c
-
+
=
-
+
=
=
0
1

## Slide 14: Synthesizing Logic that Computes on Stochastic Bit Streams
1,1,0,1,0,1,1,0,…
1,0,0,0,1,1,0,0,…
combinational logic
0,1,1,0,1,0,1,0,…
0,1,1,0,1,0,0,0,…
1,0,0,0,0,0,1,0,…
1,0,1,1,0,1,1,1,…
Applicable to arbitrary arithmetic functions
Gamma Correction Function
Notes: In today’s talk, I will cover two topics. The first topic is …
I proposed a general method to synthesize arbitrary arithmetic functions with this paradigm
An example I used in the talk is the gamma correction function and I’ll return to this example in the talk.

## Slide 15: Stochastic Logic
Probability values are the input and output signals.
combinational circuit
0.7
0.616

## Slide 16: Stochastic Logic
combinational circuit
Probability values are the input and output signals.
t
Functions of a probability value t.
3
.
0
8
.
0
8
.
0
2
+
-
t
t

## Slide 17: Mathematical Model
combinational logic
X2
X1
Xn
Independent
Random
Boolean
Variables
Y
Random
Boolean
Variable
?
Notes: Mathematically, I’m considering combinational logic, built with AND, OR, assume that they are prefect, no defect in them.

## Slide 18: Bernstein Polynomial
Bernstein basis polynomial of degree n
Bernstein polynomial of degree n
is a Bernstein coefficient

## Slide 19: Bernstein Polynomial
Obtain Bernstein coefficients from power-form coefficients:
Given
, we have

## Slide 20: Bernstein Polynomial
Elevate the degree of the Bernstein polynomial:
Given
, we have

## Slide 21: Example: Converting a Polynomial
Power-Form Polynomial
Bernstein Polynomial
coefficients in unit interval

## Slide 22: Synthesizing Circuit to Implement Polynomial
Power-Form Polynomial
Bernstein basis polynomial
Bernstein polynomial of degree 2
Bernstein coefficient
Step 1: Convert the polynomial into a Bernstein form.

## Slide 23: Synthesizing Circuit to Implement Polynomial
Power-Form Polynomial
Step 2: Elevate the Bernstein polynomial until all coefficients are in the unit interval.
less than 0
coefficients all in unit interval
Step 3: Implement this with “generalized multiplexing.”
Step 1: Convert the polynomial into a Bernstein form.

## Slide 24: Synthesizing Circuit to Implement Polynomial
Power-Form Polynomial
(Evaluate on t = 1/2)
P(Xi=1) = t (= 1/2)
P(Zi=1) = bi,3
(Bernstein
Coefficient)
g(1/2) = 1/4

## Slide 25: Generalized Multiplexing
(0 ≤ bi,n ≤ 1)
P(Xi=1) = t
P(Zi=1) = bi,n
Independent
Notes: The logic is traditional combinational logic

## Slide 26: Mathematical Contributions
U is the set of polynomials that can be implemented by logical computation on stochastic bit streams.
V is the set of polynomials that can be represented as Bernstein polynomial with coefficients in the unit interval.
W is the set of polynomials g(t) such that
  Either g(t) ≡ 0 or ≡ 1
  Or 0 < g(t) < 1, for all 0 < t < 1, and 0 ≤ g(0), g(1) ≤ 1
Practical Implication:
A necessary and sufficient condition on whether polynomials can be implemented by logical computation on stochastic bit streams.
A guarantee that degree elevation will produce Bernstein polynomials with coefficients in the unit interval.
Theorem:
“Uniform Approximation and Bernstein Polynomials with Coefficients in the Unit Interval”
W. Qian, M. Riedel, and I. Rosenberg
European Journal of Combinatorics, 2011
Notes: Challenge part is U = W, using a combination of combinatorics, real analysis, polynomial theory to prove. A contribution in polynomial theory.

## Slide 27: Non-Polynomial Functions
Find a Bernstein polynomial with coefficients in the unit interval that approximates the non-polynomial g(t).
Find real values to minimize
subject to
Solved by quadratic programming

## Slide 28: Example: Gamma Correction Function
Coefficients of Degree-6 Bernstein polynomial approximation:
b0,6 = 0.0955, b1,6 = 0.7207, b2,6 = 0.3476, b3,6 = 0.9988,
b4,6 = 0.7017, b5,6 = 0.9695, b6,6 = 0.9939

## Slide 29: Fault Tolerance
Stochastic Encoding
  A bit flip does not substantially change the probability:
  1010111001 → 1010011001
Binary Radix Encoding
  A bit flip in the most significant bit causes a huge change in the value:
  (1010)2 → (0010)2
0.6
0.5
10
2

## Slide 30: Fault Tolerance
Implementing arithmetic function y=x1x2s+x3(1−s) for x1=4/8, x2=6/8, x3=7/8 and s=2/8. 10% noise injection.
Small error!
Large error!
Stochastic Implementation
Deterministic Implementation
Notes: The deterministic design consists of adder and multiplier and the number is represented in binary radix encoding
The reason that the stochastic logic can tolerate fault better than deterministic design is that:
In the stochastic encoding, each bit is of the same significance and a bit flip only cause a small change on the number
For the deterministic design, the number is represented as the binary radix encoding, if the most significant bit gets flipped, a large error occurs.

## Slide 31
Deterministic v.s. Stochastic Implementation of Gamma correction function with 10% noise injection.
Conventional Implementation
Stochastic Implementation
1%
2%
10%
Stochastic Implementation: no pixels with errors > 25%!
Deterministic implementation: 37% pixels with errors > 25%

## Slide 32: Hardware Cost Comparison
Compare conventional implementation to stochastic implementation of polynomial functions.
Mapped onto FPGA (counting the number of LUTs)
Conventional implementation: 10-bit binary radix
Stochastic implementation: bit stream of length 210

## Slide 33: Comparison of Fault Tolerance for Mathematical Functions
Sixth-order Maclaurin polynomial approx., 10 bits:
sin(x), cos(x), tan(x), arcsin(x), arctan(x), sinh(x),
cosh(x), tanh(x), arcsinh(x), exp(x), ln(x+1)

## Slide 34: Sequential Constructs
What about complex functions such as tanh, exp, and abs?

## Slide 35: Sequential Constructs

## Slide 36: Sequential Constructs

## Slide 37: Sequential Constructs

## Slide 38: Sequential Constructs

## Slide 39: Sequential Constructs

## Slide 40: Sensing Applications
Median Filter-Based Image Noise Reduction

## Slide 41: Sensing Applications
Frame Difference-Based Image Segmentation

## Slide 42: Sensing Applications
Image Contrast Enhancing

## Slide 43: Sensing Applications
Kernel Density Estimation-Based Image Segmentation

## Slide 44: Comparison of Encoding
Spectrum of Encoding
Binary Radix Encoding
Stochastic Encoding
 | Binary Radix Encoding | Stochastic Encoding
Circuit Area | Large | Small
Error Tolerance | Bad | Good
Delay | Short | Long
(Positional)
(Uniform, Long Stream)
(Not compact,
Long Stream)
(Compact,
Efficient)
(Positional, Weighted)
(Uniform)

## Slide 45: Future Directions
Spectrum of Encoding
Binary Radix Encoding (Compact, Positional)
Stochastic Encoding
(Not compact, Uniform)
?
Possible encodings in the middle with the advantages of both?
Notes: A mixture of encoding.

## Slide 46
Acknowledgements
Kia Bazargan
David Lillja
Weikang Qian
Ramesh Harjani
Peng Li

## Slide 47: Switch-based Boolean computation
Shannon’s work: A Symbolic Analysis of Relay and Switching Circuits(1938)

## Slide 48: 1D and 2D switches

## Slide 49: A lattice of 2D switches
3 × 3 2D switching network and its lattice form

## Slide 50: Boolean functionality and paths
Switches are controlled by Boolean literals.
fL evaluates to 1 iff there exists a top-to-bottom path.
gL evaluates to 1 iff there exists a left-to-right path.

## Slide 51: Logic synthesis problem
How can we implement a given target Boolean function fT with a lattice of 2D switches?
Example: fT = x1x2x3+x1x4

## Slide 52: Logic synthesis problem
Example: fT = x1x2x3+x1x4+x1x5
9 TOP-TO-BOTTOM PATHS!

## Slide 53: Boolean Function Duality
Given:
Obtain:

## Slide 54: Our synthesis method
Example: fT = x1x2x3+x1x4+x1x5
fTD = (x1+x2+x3)(x1+x4)(x1+x5)
fTD = x1 + x2x4x5 + x3x4x5
Obtain the dual of fT.
Assign each product of fT to a column.
Assign each product of fT D to a row.
Compute an intersection set for each site.
Arbitrarily select a literal from an intersection set and assign it to the corresponding site.

## Slide 55: Our synthesis method

## Slide 56: Our method’s performance
Area of the lattice: m×n
The time complexity:
O(m2n2)
n and m are the number of products of the target function fT and its dual fTD, respectively.

## Slide 57: Computing with Defects
57
Ideally, if the applied voltage is 0, then all the crosspoints are OFF and so there is no connection between any of the plates.
Ideally, If the applied voltage is VDD, then all the crosspoints are ON and so the plates are connected.
With defect in nanowires, not all crosspoints will respond this way.

## Slide 58: Implementing Boolean functions
58
signals in: Xij’s
signals out: connectivity top-to-bottom / left-to-right.

## Slide 59: An example with 16 Boolean inputs
59
A path exists between top and bottom, f = 1

## Slide 60: Non-Linearities
From vacuum tubes, to transistors, to carbon nanotubes, the basis of digital computation is a robust non-linearity.
signal in
signal out
Holy Grail

## Slide 61: Percolation Theory
Rich mathematical topic that forms the basis of explanations of physical phenomena such as diffusion and phase changes in materials.
Sharp non-linearity in global connectivity as a function of random local connectivity.
Random Graphs
Broadbent & Hammersley (1957); Kesten (1982); and Grimmett (1999).
61

## Slide 62: Percolation Theory
Poisson distribution of points with density λ
Points are connected if their distance is less than 2r
Study probability of connected components
S
D

## Slide 63: Percolation Theory
There is a phase transition at a critical node density value.
63

## Slide 64: Non-Linearity Through Percolation
64
p2 versus p1 for 1×1, 2×2, 6×6, 24×24, 120×120, and infinite size lattices.
Each square in the lattice is colored black with independent probability p1.
p2 is the probability that a connected path exists between the top and bottom plates.
p1
p2

## Slide 65: Margins
65
One-margin: Tolerable p1 ranges for which we interpret p2 as logical one.
Zero-margin: Tolerable p1 ranges for which we interpret p2 as logical zero.
Margins correlate with the degree of defect tolerance.

## Slide 66: Margin performance with a 2×2 lattice
66
f =X11X21+X12X22
g =X11X12+X21X22
Different assignments of input variables to the regions of the network affect the margins.
X11 | X21 | X12 | X22 | f | Margin | g | Margin
0 | 0 | 0 | 0 | 0 | 40% | 0 | 40%
0 | 0 | 0 | 1 | 0 | 25% | 0 | 25%
0 | 0 | 1 | 1 | 1 | 14% | 0 | 23%
0 | 1 | 0 | 1 | 0 | 23% | 1 | 14%
0 | 1 | 1 | 0 | 0 | 0% | 0 | 0%
0 | 1 | 1 | 1 | 1 | 14% | 1 | 14%
1 | 1 | 1 | 1 | 1 | 25% | 1 | 25%

## Slide 67: One-margins (always good)
67
Defect probabilities exceeding the one-margin would likely cause an (1→0) error.
f =1
f =0
ONE-MARGIN

## Slide 68: Good zero-margins
68
Defect probabilities exceeding zero-margin would likely cause an (0→1) error.
f =0
f =1
ZERO-MARGIN

## Slide 69: Poor zero-margins
69
Assignments that evaluate to 0 but have diagonally adjacent assignments of blocks of 1's result in poor zero-margins
f =0
f =1
POOR
ZERO-MARGIN

## Slide 70: Lattice duality
Note that each side-to-side connected path corresponds to the AND of the inputs; the paths taken together correspond to the OR of these AND terms, so implement a sum-of-products expression.
A necessary and sufficient condition for good error margins is that the Boolean functions corresponding to the top-to-bottom and left-to-right plate connectivities f and g are dual functions.

## Slide 71: Lattice duality

## Slide 72: Future work
We are investigating our method’s applicability to different technologies.
We are studying the applicability of the math to the problem of testing whether two given monotone Boolean functions are mutually dual.

## Slide 73: Thank You!