## Slide 1: A Scalable Deterministic Approach to Stochastic Computing
Yadu Kiran, Electrical & Computer Engineering
Advisor: Marc Riedel

## Slide 2: An Introduction to Stochastic Computing
Stochastic computing revolves around a non-positional encoding for numbers.
Numbers are represented as fractional values.
Operations are performed on randomly generated bitstreams.

## Slide 3: Representing Values
Binary:
  A , can represent distinct values
Stochastic:
Bitstream Generator
  A can only represent distinct values.

## Slide 4: A Multiply Circuit
A 4-bit Multiplier
A Stochastic Multiplier
AND
1,1,0,1,0,1,1,1
a = 6/8
b = 4/8
c = 3/8
1,1,0,0,1,0,1,0
1,1,0,0,0,0,1,0
An AND gate produces an output 1 only when both its inputs are 1.

## Slide 5: Scaled Addition and Arbitrary Polynomials
4/5
3/5
3/5
2/5

## Slide 6: *
  Randomness is neither free nor cheap!

## Slide 7: Advantages and Drawbacks
Stochastic Computing is innately fault-tolerant.
  But requires more bits to represent the same range of values.
Circuit structures are simpler than their binary counterparts
  But they are not perfectly accurate.
Accuracy can be improved by using longer bit-streams.
  But this results in longer latency.
AND
1,1,0,0,1,1,0,1
a = 6/8
b = 4/8
c = 1/8
0,1,0,1,0,0,1,0
0,1,0,0,0,0,0,0

## Slide 8: But is randomness necessary?
90-95% of the circuit area is dedicated to generating those random bit-streams.
Jenson and Riedel demonstrated that by generating bit streams deterministically, one can obtain perfectly accurate results.
(A deterministic approach to stochastic computation, ICCAD 2016)
Every bit of one operand must be matched up against every bit of the second operand(s) exactly once.

## Slide 9: Deterministic approach
This could be achieved by three techniques:
  Rotation
  Clock-Division
  Relatively Prime Length Bit Streams
Clock-Division Method

## Slide 10: Putting it together
A
B
Bit-stream A
Bit-stream B
Counter
Counter
CLK
1000 1000 1000 1000
1111 1111 1111 0000
1000 1000 1000 0000
1/4 1000
3/4 1110

## Slide 11: The Thermometer Encoding
All the 1’s are grouped together and appear consecutively, as well as all the 0’s.
This encoding is not a requirement, but a consequence of the circuit used to generate deterministic bit streams.

## Slide 12: Problem solved?
The Deterministic Approach solves the problem of inaccuracy
But it does not solve the issue of long latency.
The number of bits at the output is the product of the number of bits of all its inputs
This is a mathematical requirement for full precision.
But this exponential increase in latency becomes intolerable for large circuits.

## Slide 13: Goal
For a given set of input operands of length , compute the output as in clock cycles, producing the most mathematically accurate result possible

## Slide 14: An Example
We cannot afford to go to 256 bits.
We want a design that always produces , and not , nor , nor

## Slide 15: A naïve attempt
The length of the output bit-stream is proportional to the size of the input bit-stream.
11 11 11 00 00
1 1 1 0 0
Original bit-stream
Down-sampled bit-stream
The downscaled/downsampled bit-stream is an approximation, and we run into errors again.

## Slide 16: Back to our Example
Downscaling each operand by 4 bits.
1111 1000 0000 0000
1111 1111 1111 1110
1 0 0 0
1 1 1 1
Original bit-stream
Down-sampled bit-stream
With Optimal Approximation and
1000 1000 1000 1000
1000 1000 1000 1000
1111 1111 1111 1111
Even with optimal approximations, our result is not ideal.

## Slide 17: A Better Attempt
Exploit the predictable nature of Thermometer Encodings
11 11 10 00 00
1 1 1 0 0
Original bit-stream
Down-sampled bit-stream
11 11 10 00 00
Original bit-stream
Sampled bit = 1
Sampled bit = 0
11 11 10 00 00
1 1 0 0 0
Original bit-stream
Down-sampled bit-stream

## Slide 18: The Example
Down-scaled bit-stream
1111 1000 0000 0000
Original bit-stream
Rounding down
1000
(Under -Approximation)
1111 1111 1111 1110
Rounding down
1110
(Under -Approximation)

## Slide 19: The Example
(
1000 1000 1000 1000
1111 1111 1111 0000
(
Error = 1
Error = 3
The bits that we highlighted are carrying partially incorrect information.
The bit is repeated in the clock-division process.
Use this opportunity to correct those erroneous bits by inverting them.

## Slide 20: The Example
  We need to invert the erroneous 0, 1 out of the 4 times it is repeated
  We need to invert the erroneous 0, 3 out of the 4 times it is repeated
The bit-flips need to happen in the right proportion with respect to the other operand!
1000 1000 1000 1000
1111 1111 1111 0000

## Slide 21: The Example
This is another stochastic multiply operation!
1000 1000 1000 1000
1111 1111 1111 0000
1100 1000 1000 1000
1111 1111 1111 1110

## Slide 22: With Error Compensation!
1100 1000 1000 1000
1100 1000 1000 1000
1111 1111 1111 1110
This matches our ideal answer!

## Slide 23: The cost of additional multiplication
We need to determine which bits to invert before we do the main operations.
Computing which bits to invert, requires the same number of clock cycles as our main operation
This doubles our latency.

## Slide 24: Not as bad as it seems!
The multiply operation to determine which bits to invert, is independent of the main operation.
Let’s Pipeline it! Throughput remains the same.
Determining errors and Downscaling is accomplished by bit shifts

## Slide 25: The Final Circuit

## Slide 26: The Final Circuit
- bit Counter
- bit Comparator
- bit Register
- bit Counter
- bit Comparator
- bit Register
Module
A’
B’
Final Output Bitstream
CLK

## Slide 27: Comparisons
We evaluated our methods against the conventional stochastic techniques that employ LFSRs, and Sobol Sequences.
Note: 0 error is not possible as we are losing the precision in terms of bits and the values we can represent.

## Slide 28: Comparisons

## Slide 29: Complex functions

## Slide 30
Thank You!
Questions?

## Slide 31: Multiplication with Partial Products